## Slide 1: SnapMirror Business Continuity (SM-BC)
Oracle Architectures
May 2021
Notes: The Finance industry for example, requires two exact copies of their enterprise data. So that, when failure renders the primary copy unavailable, the hosts can seamlessly failover to the secondary copy. Essentially to achieve zero data loss or 0 Recovery Time Objective (RTO) with 0 Recovery Time Objective (RTO).
SM-BC is the 0 RPO 0 RTO SAN data protection solution which provides transparent application failover (TAF) to the secondary storage cluster upon unavailability of the primary storage cluster. Therefore enabling business continuity for Tier-1 applications.
Comparing SM-BC to SnapMirror Synchronous (SM-S):
SM-S supports both SAN and NAS protocols. And SM-S supports SAN with different LUN identities on the source and destination. The copies are totally independent from the host SCSI stack perspective and no correlation is made in MPIO layer between the copies. With SM-S, you need to manually failover or create orchestration scripts for overall application failover to establish the link between the application and the RPO 0 copy so that application can continue the operation seamlessly after a disaster. Now, SM-BC enables automated failover for business-critical applications, without any manual intervention.
Quick glimpse of the what SM-BC solves?
It maintains the LUN identity between the two copies, so the application sees this as a shared entity. And application granularity is enabled using consistency group (CG), with automatic transparent failover (RTO 0) to the secondary copy at this CG level. All in all, seamless failover to the application, with no data loss.

## Slide 2: Agenda
  SMBC maximums
  Oracle Deployment Architectures
  Supported testcases
  Unsupported configs
  Data protection
Notes: So what you will learn today is:
Why do you need data protection?
What is business continuity (BC)?
SnapMirror Business Continuity (SM-BC) overview
Near-zero RTO with transparent application failover (TAF)
Zero Data Loss with SnapMirror Synchronous (SM-S)
SM-BC Vs. MetroCluster (MCC)

## Slide 3: Impact radius
Demarcation for SMBC vs MCC
Localized power outages
Primary site
Cluster A
Local
< 1-2km
Metro
< 150km
Regional
300 -700 km
Floods, storms, and earthquakes
Major disasters
Far disaster recovery site
Cluster C
Near disaster recovery site
Cluster B
Notes: Disasters happen.
At first, you need to have clarity on what exactly you are protecting against and what the disaster impact radius is?
In today’s constantly connected global business environment, planning for business continuity is key.
    Be it unplanned events that can range from disasters.
To planned events such as DR Testing, Tech Refresh, Maintenance, etc.

## Slide 4: SMBC Synchronous replication for zero data loss
Master CG NVRAM
Mirror CG NVRAM
Host write (1)
RACK (3)
Write (2)
ACK (4)
Write (2)
Master CG NVRAM
Host write (1)
ACK (4)
ACK (6)
Proxy write (2)
Write (3)
Mirror CG NVRAM
RACK (5)
Host write to a CG on cluster hosting master copy
Host write to a CG on cluster hosting mirror copy
Write (3)
ALUA
ALUA
Cluster A
Cluster B
Cluster B
Cluster A
Notes: Mirroring all writes to mirrored vols with snapshots taken hourly
ALUA based transparent failover

## Slide 5: ONTAP Mediator 2.0
Linux physical or virtual server running Red Hat Enterprise Linux (RHEL) or CentOS 7.6 – 8.2
Establish quorum
  Both NetApp® ONTAP® systems (including nodes) periodically send heartbeat and status of replication
Avoid split-brain
  Scenario in which each cluster may simultaneously try to become the master
Orchestrates automated failover upon detection of failure
  Switchover of application host with RTO <= 120 seconds
NetApp® ONTAP® Mediator service can manage a total of 10 cluster pairs
Enables automated failover during disaster
Replication status
Primary data center
Secondary data center
ONTAP Mediator
Third site
Notes: ONTAP Mediator 1.2 software is distributed through NetApp software portal. ONTAP Mediator version 1.2 is to be downloaded and installed on RHEL / CentOS Linux 7.6 to 8.1 (on-prem bare metal or VM). The ONTAP Mediator host must be accessible by both SMBC clusters.
The ONTAP Mediator is an application provisioned on a Linux host physical or virtual in a failure domain, separate from the two ONTAP clusters
The ONTAP Mediator monitors the pulse of the storage systems in either cluster and cluster interconnectivity to ensure they are online and healthy.
It records heart beats from the nodes of the clusters and is aware of the state of the clusters. The ONTAP Mediator helps establish quorum and helps protect from ‘Split Brain’ scenario where every node, due to network or disk heartbeat failure with other nodes in the cluster, assumes that it is the sole surviving member of the Cluster thereby proclaiming itself to be the Master. The ONTAP Mediator essentially prevents creating multiple masters and avoids such situation which causes the enterprise application data at each site to get out of sync and in a position where they cannot be resynchronized.
This ONTAP Mediator establishes Quorum Consensus such that, in the steady state while the relationship is “In sync”. Here, the Primary CG serves IO and replicates the incoming IO to Mirror CG. The relationship can go “Out of sync” due to various reasons like InterCluster link going down, or one of the clusters becoming unavailable due to network outage, power outage or other reasons. During this “Out of sync” condition, the copy having 'consensus' has the authority to serve IO. Consensus is defined as 2 out of 3 votes in the quorum constituting Primary, Mirror and ONTAP Mediator.
Note that Primary can also get the consensus without ONTAP Mediator by marking the Mirror as failover-incapable which provides it two votes.
Primary Bias or Primary First Principle - The Primary CG is given a preference in getting consensus as it is the one currently serving IO. The Mirror CG honors the Primary-bias by implementing a non-aggressive behavior in claiming consensus and gives the Primary CG a chance to claim it first.
Most importantly it automatically orchestrates a failover in case of a disaster
ONTAP Mediator 1.2 is common between MCC IP and SMBC, a single distribution supports both MCC IP and SMBC. MCC IP uses a combination of iSCSI / REST APIs, whereas SMBC uses a set of REST API services. MCC IP and SMBC use different Mhost CLI commands to configure ONTAP Mediator.
Note: By default, ONTAP Mediator provides the service in port 31784. Hence Port 31784 should be open between ONTAP and ONTAP Mediator.
Without the ONTAP Most Mediator, planned and unplanned failover will not be possible.
SMBC_A::*> snapmirror ONTAP Mediator show
ONTAP Mediator Address Peer Cluster Connection Status Quorum Status
---------------- ---------------- ----------------- -------------
10.236.172.86 SMBC_B connected true
SMBC_B::*> snapmirror ONTAP Mediator show
ONTAP Mediator Address Peer Cluster Connection Status Quorum Status
---------------- ---------------- ----------------- -------------
10.236.172.86 SMBC_A connected true
SMBC_B::*> snapmirror show -expand
Progress
Source Destination Mirror Relationship Total Last
Path Type Path State Status Progress Healthy Updated
----------- ---- ------------ ------- -------------- --------- ------- --------
vs0:/cg/cg1 XDP vs1:/cg/cg1_dp Snapmirrored InSync - true -
vs0:vol1 XDP vs1:vol1_dp Snapmirrored InSync - true -
2 entries were displayed.
SMBC_A::*> volume show -fields is-smbc-master,smbc-consensus,is-smbc-failover-capable -volume vol1
vserver volume is-smbc-master is-smbc-failover-capable smbc-consensus
------- ------ -------------- ------------------------ --------------
vs0 vol1 true false Consensus
SMBC_B::*> volume show -fields is-smbc-master,smbc-consensus,is-smbc-failover-capable -volume vol1_dp
vserver volume is-smbc-master is-smbc-failover-capable smbc-consensus
------- ------- -------------- ------------------------ --------------
vs1 vol1_dp false true No-consensus

## Slide 6
Primary data center
Secondary data center
ONTAP Mediator
Third site
SnapMirror
Business continuity

## Slide 7: Host path to LUNs
Asymmetric Logical Unit Access (ALUA) provides host optimal path to the LUN
ALUA
SVM
SVM
Master CG
Mirror CG
Active nonoptimized
Active optimized
Common LUN ID across copies
Proxy path
Cluster A
Cluster B
Notes: Transparent application failover uses SCSI Asymmetric Logical Unit Access (ALUA), an industry standard protocol for identifying available and optimized paths between a storage system and applications hosts. ALUA allows the initiator to query the target about path attributes, such as active optimized and active unoptimized paths and allows the target to communicate events back to the initiator.
For the Application Host(s) or Host-cluster to be able to transparently failover to another copy,
Both the source and destination Volume\LUN copies should be visible as shared storage (by preserving the unique SCSI target identity)
The Application Host(s) or Host-cluster should view this single shared storage endpoint with multiple paths and reports path state changes across clusters seamlessly.
Transparent application failover is achieved by replicating path related information and presenting a unique SCSI target id space so that the information is presented by all source and destination cluster nodes when the host issues the Report Target Port Groups (RTPG) command.

## Slide 8: Planned failover
Host accesses LUN using newly designated optimized path in planned failover
Master CG
Mirror CG
ALUA
In Sync
Initiate failover
Mirror CG
Master CG
ALUA
In sync
Active nonoptimized
Active optimized
Active optimized
Active nonoptimized
Change in path state
Change in CG state
CG on Cluster A
CG on Cluster B
CG on Cluster A
CG on Cluster B
Notes: You can perform a Planned Failover (PFO) operation initiated by the secondary cluster admin, by which the primary/mirror roles of primary and secondary are swapped without disrupting client IO. The secondary starts serving IO locally (Active Optimized Path) and primary will start proxying IO to the secondary. There may be a few seconds of IO no-progress. The purpose of a planned failover could be to perform maintenance operation on the primary cluster or to periodically test the secondary copy.
The requirements and high-level steps are mentioned below.
Planned failover can be triggered from the secondary ONTAP cluster.
The critical window (IO outage window from ONTAP perspective) for a single CG (max 12 volumes) shall be less than 10 seconds.
The critical window (IO outage window from ONTAP perspective) for 5 CGs (max 12 volumes per CG) shall be less than 30 seconds.
No time guarantees for the resumption and completion of Zero RPO protection in the reverse direction (flip-resync).
A best effort common snapshot is taken before the PFO workflow starts. This helps in speeding up the flip resync in case of success as well as the forward resync in case of failure. This snapshot is not redirected nor the older snaps are rotated out to reduce the latency.
Monitoring:
ClusterB::> snapmirror failover start -destination-path vs1:/cg/dcg1
[Job 56] Job is queued: SnapMirror failover for destination "vs1:/cg/dcg1".
ClusterB::*> snapmirror failover show -instance
Source Path: vs0:/cg/scg1
Destination Path: vs1:/cg/dcg1
Failover Status: started
Error Reason:
Start Time: 5/11/2020 20:58:26
End Time: -
Primary Data Cluster: ClusterA
Last Progress Update:
Failover Type: planned
Error Reason codes: -
ClusterB::*> snapmirror failover show -instance
Source Path: vs0:/cg/scg1
Destination Path: vs1:/cg/dcg1
Failover Status: started
Error Reason:
Start Time: 5/11/2020 20:58:26
End Time: -
Primary Data Cluster: ClusterB
Last Progress Update: Role change completed and sync protection is aborted.
Failover Type: planned
Error Reason codes: -
ClusterB::*> snapmirror failover show -instance
Source Path: vs0:/cg/scg1
Destination Path: vs1:/cg/dcg1
Failover Status: completed
Error Reason:
Start Time: 5/11/2020 20:58:26
End Time: 5/11/2020 20:58:41
Primary Data Cluster: ClusterB
Last Progress Update: Sync protection resumption in progress
Failover Type: planned
Error Reason codes: -
Once the fail-over operation is complete, the status of sync protection can be monitored from the new destination cluster
ClusterA::*> snapmirror show
Progress
Source Destination Mirror Relationship Total Last
Path Type Path State Status Progress Healthy Updated
----------- ---- ------------ ------- -------------- --------- ------- --------
vs1:/cg/dcg1 XDP vs0:/cg/scg1 Snapmirrored InSync - true -
Rollback will kick in if the PFO workflow is not able to complete the critical window within the stipulated time, the primary triggers a role back by which the it reclaims the ownership and resume serving IO.
Any errors or delays in converting the role will result in a rollback operation and the completion of rollback can be ascertained by viewing the state of the protocol fence on each of the primary volumes.
ClusterA::*> snapmirror failover show -instance
Source Path: vs1:/cg/dcg1
Destination Path: vs0:/cg/scg1
Failover Status: started
Error Reason:
Start Time: 5/11/2020 21:18:22
End Time: -
Primary Data Cluster: ClusterB
Last Progress Update: Sync protection is active, and I/O is suspended
Failover Type: planned
Error Reason codes: -
ClusterB::*> volume show -fields is-protocol-access-fenced
vserver volume is-protocol-access-fenced
------------------- ------ -------------------------
vs1 dvol1 true
ClusterA::*> snapmirror failover show -instance
Source Path: vs1:/cg/dcg1
Destination Path: vs0:/cg/scg1
Failover Status: failed
Error Reason: Tiebreaker rejected the operation.
Start Time: 5/11/2020 21:18:22
End Time: 5/11/2020 21:18:44
Primary Data Cluster: ClusterB
Last Progress Update: Sync protection is active and I/O is suspended
Failover Type: planned
Error Reason codes: 6622018
ClusterB::*> vol show -fields is-protocol-access-fenced
vserver volume is-protocol-access-fenced
------------------- ------ -------------------------
vs1 dvol1 false

## Slide 9: Unplanned failover during the event of a disaster
ONTAP Mediator initiates the automatic transparent failover
Master CG
Mirror CG
ALUA
In sync
Master CG
ALUA
Active non-optimized
Active optimized
Active optimized
CG on Cluster B
CG on Cluster A
CG on Cluster B
Notes: Automatic unplanned failover (AUFO), also called as ONTAP Mediator-assisted AUFO operation occurs when the primary cluster is down or isolated. This operation can only be performed with the assistance of ONTAP Mediator where the secondary cluster gets converted to primary and starts serving IO locally.
The ONTAP Mediator runs a health check of the primary, secondary ONTAP clusters as well as Inter-cluster (IC) paths. If both paths report that the primary cluster is down or isolated due to network failures, the ONTAP Mediator will initiate an unplanned failover to activate the secondary cluster.
The status of the Unplanned failover operation can be monitored with the below command:
cluster-2::*> snapmirror failover show -instance
Start Time: 9/23/2020 22:03:29
Source Path: vs1:/cg/scg3
Destination Path: vs3:/cg/dcg3
Failover Status: completed
Error Reason:
End Time: 9/23/2020 22:03:30
Primary Data Cluster: cluster-2
Last Progress Update: -
Failover Type: unplanned
Error Reason codes: -
cluster-2::*>
The status of the conversion for each volume in the group can be confirmed with the below command:
cluster-2::*> volume show dvol3 -fields smbc-consensus,is-smbc-master,is-smbc-failover-capable,type
vserver volume type is-smbc-master is-smbc-failover-capable smbc-consensus
------- ------ ---- -------------- ------------------------ --------------
vs3 dvol3 RW true capable, type Consensus
cluster-2::*> snapmirror show
Progress
Source Destination Mirror Relationship Total Last
Path Type Path State Status Progress Healthy Updated
----------- ---- ------------ ------- -------------- --------- ------- --------
vs1:/cg/scg3
XDP vs3:/cg/dcg3 Broken-off
Idle - false -
Monitor the events resulting in a ONTAP Mediator action with the below command. Note: This is available in diagnostic privilege only.
cluster-2::*> snapmirror ONTAP Mediator action-log show
CG Name Token Operation Contype Result Start Time Clonotype Taken(ms)
--------- ------- ---------- ------- --------- -------------- -------------
scg3.2 44 consensus boot stop 9/24/2020 00:06:37
994
scg3.2 46 oos - failover-incapable
10/1/2020 10:30:55
6273
scg3.2 49 oos - auto-failover
10/1/2020 12:26:08
11705

## Slide 10: Use cases
Oracle Apps

## Slide 11: Granular Application availability
NetApp® SnapMirror® business continuity
Site A
Site B

## Slide 12: Asymmetric platform configuration solution
Asymmetric platform flexibility –High end primary cluster while entry-level platform on secondary
Poor Man’s DR
NetApp® SnapMirror® business continuity
Site A
Site B
Production application
Mirror copy
Notes: SM-BC enables an optimal design targeted for your specific requirements
On site A you have multiple database applications only one of which is critical for the business, while at site B there are only few services and it hosts the mirror of the critical application on A
So instead of having a high end platform at both sites, you could choose to have a high end at site A and entry at site B, and likewise have different shelf and drives on both clusters
You can also make use of the mirror copy, perform test/dev operations

## Slide 13: Remote Office & Branch office
Protect critical applications in remote offices
Mirroring the dataset to a central site optimizes capital expenditure (capex) and operational expenditures (opex)
Metro deployment
City A
City B
City D
City C
City E
State
Notes: SM-BC enables several new use cases for business continuity
Regulations for financial institutions in some countries requires businesses to periodically prove the serviceability of their secondary data centers, for this reason workloads must be served periodically from the primary as well secondary data center, SM-BC facilitates such a deployment
One of our major customers with numerous remote offices wanted to provide business continuity for the core applications at each remote office, but did not want the overhead of additional hardware and operational management cost at each office. This is now possible using SM-BC.

## Slide 14: Tik Tok deployments/ Seamless switchover deployment
  Alternately run workloads from primary and secondary by switching over instead of failover
Switch specific workloads across site as per Institutional Guidelines
Serve critical workloads alternately from two sites
Notes: SM-BC enables several new use cases for business continuity
Regulations for financial institutions in some countries requires businesses to periodically prove the serviceability of their secondary data centers, for this reason workloads must be served periodically from the primary as well secondary data center, SM-BC facilitates such a deployment
One of our major customers with numerous remote offices wanted to provide business continuity for the core applications at each remote office, but did not want the overhead of additional hardware and operational management cost at each office. This is now possible using SM-BC.

## Slide 15: Cross DR deployments for granular set of applications
Maximum utilization of controller and availability of applications
Serve critical workloads
from two sites
SMBC CG1
SMBC CG2
SMBC CG3
CG
Consistency Group
Notes: SM-BC enables several new use cases for business continuity
Regulations for financial institutions in some countries requires businesses to periodically prove the serviceability of their secondary data centers, for this reason workloads must be served periodically from the primary as well secondary data center, SM-BC facilitates such a deployment
One of our major customers with numerous remote offices wanted to provide business continuity for the core applications at each remote office, but did not want the overhead of additional hardware and operational management cost at each office. This is now possible using SM-BC.

## Slide 16: Oracle environment with ASM mirroring & SMBC using Extended RAC
RAC1
RAC2
ASM DATABASE (Mirroring)
Site A
Site B
PRIVATE
ASM Mirrored
Devices
Oracle CG Container
HOME,
GRID
DATABASE
Virtual
Machine Disk
HOME,
Grid
DATABASE
Virtual
Machine Disk
Quorum Votedisk
OCR I/O
Database I/O
Non-optimized path

## Slide 17: Oracle TR PURPOSE –
RAC1
RAC2
SMBC
Oracle Database
PRIVATE
Oracle CG Container
HOME,
GRID
DATABASE
Virtual
Machine Disk
HOME,
Grid
DATABASE
Virtual
Machine Disk
Optimized
Non-Optimized
Consistency Group
CG

## Slide 18: Oracle Extended RAC without ASM mirroring & SMBC (using votedisk majority)
RAC1
SMBC
ORACLE DATABASE
Site A
Site B
PRIVATE
VOTE Disk FG1
RAC2
RAC4
RAC3
Site C
Quorum
OCR+VOTE Disk
VOTE Disk FG2
ERP
HOME,
GRID
DATABASE
Virtual
Machine Disk
HOME,
Grid
DATABASE
Virtual
Machine Disk
CRM
DB services
OCR I/O
ERP DB I/O
CRM DB I/O
Non-optimized path
Non-optimized path
Oracle CG Container
SMBC +Mediator

## Slide 19: TR Purpose - Oracle Database over SMBC uniform access
SMBC
ORACLE DATABASE
Primary
Secondary
Optimized
Non- Optimized

## Slide 20: 3-way DR /Three Site DR
Prod. - SVM
Cluster A
Cluster B
Primary CG
NDR - SVM
Mirror CG
SM-BC
SM-async
Cluster C
DR
Notes: Consistency Group (CG) - In a relationship created to protect for business continuity, a Consistency Group (CG) is defined as a collection of FlexVols that provide a strong Consistency guarantee for the application workload which needs to be protected for business continuity. In regular deployment, the group of volumes picked to be part of a CG will map to an application instance. The SM-BC relationship (termed a CG Relationship) can be established between a source CG and a destination CG. The source and destination CGs must be isomorphic i.e. contain the same number and type of Volumes. The individual volumes, which are part of the CG will be referred to as constituents or items.
CG guarantees dependent-write order consistency across its constituents during coordinated operations like common-snapshot creation, out-of-sync, failover etc. The Primary CG on primary cluster actively serves IO and the CG on secondary cluster which is passive is designated as Mirror CG.
Note: This Consistency Group (CG) is a SnapMirror construct and not a first class ONTAP citizen as this point. What this means is that you cannot separately create CGs in ONTAP, this is only created as part of the protect for business continuity workflow only.
Single Directional Synchronous SnapMirror replication - The underlying technology used for synchronous replication is SnapMirror Synchronous (SM-S). The Application I/O going to the Primary copy is synchronously replicated to the Mirror copy using SM-S technology and maintains data consistency between the two copies of the LUN with volume granularity.
Now in an SM-BC data protection relationship, the application hosts view these LUNS protected for business continuity as a Single Virtual LUN. What this means is that the LUN Serial Number will be preserved for both copies of the LUN and thereby they appear as same virtual device to the Host through different paths - some from primary cluster and others from the secondary cluster. The active optimized(AO) path will originate from the Primary copy through the node that owns the volume, while the other paths will be active non-optimized (ANO) paths. Although in the case of ASA systems, you will have 2 active optimized paths to the Primary CG.
It CG is such that dependent set of writes 'w1' and 'w2' where 'w2' is dependent on 'w1', CG SM-Sync will guarantee that 'w2' is not available on mirror copy without 'w1' i.e. if 'w2' is present, 'w1' is also present. So, write 'w1' is issued on volume 'v1' of CG 'cg1' and 'w2' is on volume 'v2', the OOS design must ensure that if 'w1' fails to be replicated to mirror copy, then 'w2' is also not written to the mirror copy.
ALUA based path advertisement enables transparent failover capability for the application hosts.
What you need to remember is that in the first release of SM-BC, the SCSI layer on the Mirror CG copy implements Proxy Taskset Mode (PTM) to forward any incoming IO on the active non-optimized path to Primary CG over an iSCSI session. So, any IO that goes to the ANO path will be redirected to the Primary CG, so there will be performance latency.
Mirroring all writes to mirrored vols with snapshots taken hourly (by default). ALUA based transparent failover.
In ONTAP 9.8 release, fan-out configuration of a volume within the CG can be configured with an asynchronous SnapMirror relationship. User can create the fan-out with async configuration at item level of the CG relationships.
Note: However, SMBC destination endpoints are not supported in cascade topology relationship.
What you need to bear in mind however is that expand a CG (adding items to an existing SMBC CG relationship) is not supported in the ONTAP 9.8 release. The only way to change the composition of SMBC CG relationship is to delete the existing relationship and re-create it with new items/LUNs.
Note: While adding new volumes by delete and re-create of SMBC CG relationship, user should make sure that common snapshot exists between source and destination volumes.

## Slide 21: Failure scenarios
Notes: Failover is the process of activating the secondary copy by which it starts serving IO locally. The secondary's identity gets converted from mirror to primary and its paths changed from active-non-optimized to active-optimized. Failover can be of two kinds, planned (PFO – Planned FailOver) and unplanned (AUFO – Automatic UnPlanned FailOver).

## Slide 22: Normal operations
Steady state
Mediator
C1
Primary
C2
Secondary
Parameter | Details
Host access to storage | C1 and C2
NetApp® SnapMirror® business continuity relationship state | In Sync
Notes: Link failure between the sites (Split Brain)
In a split-brain scenario with Sync policy, the Primary LUN continues to serve I/O to the host while all the paths from the secondary cluster report Illegal request / LU not found for all I/O commands.
Out of Sync
Sync data path forces an Out of Sync scenario upon a persistent network failure (any transient n/w issue that is not resolved in 15 secs OR no connection between the 2 sites)
If due to any reason the relationship goes out of sync with Sync policy, the ONTAP Mediator chooses Primary as the surviving site and the Primary LUN continues to serve I/O to the Host. All the paths from the secondary cluster report Illegal request / LU not found for all I/O commands.
Now say there’s a double failure with the intersite link down and the mediator going down (either simultaneously or sequentially in the below order):
Primary to ONTAP Mediator is down
Primary to Secondary link down (relationship if out of sync) and
Due to the OOS event in this case, the primary cluster needs to re-establish consensus with agreement from either the Mediator or the peer cluster. But since neither is reachable, it cannot establish consensus to serve I/O. Thereby, there will be DISRUPTION
Although another scenario where the intersite link failure first occurs, the relationship would go out of sync. Site A gets consensus via the ONTAP Mediator, and continues to be the Primary CG and serves IO
And now if the ONTAP Mediator fails after the failover/switchover process, the second failure will have no impact except that you cannot perform planned or unplanned events during the time that the ONTAP Mediator is down.

## Slide 23: Replication link failure
Mediator
C1
Primary
C2
Secondary
Replication link failure
  Transient
  Persistent (tries 3 times every 3 seconds = 9 seconds)
Link failure between the sites (split-brain scenario)
Parameter | Details
NetApp® SnapMirror® business continuity (SM-BC) action upon failure | No action
Host access to storage | C1 after consensus
SM-BC relationship state | Out of sync
Failover operation | n/a
Notes: Link failure between the sites (Split Brain)
In a split-brain scenario with Sync policy, the Primary LUN continues to serve I/O to the host while all the paths from the secondary cluster report Illegal request / LU not found for all I/O commands.
Out of Sync
Sync data path forces an Out of Sync scenario upon a persistent network failure (any transient n/w issue that is not resolved in 15 secs OR no connection between the 2 sites)
If due to any reason the relationship goes out of sync with Sync policy, the ONTAP Mediator chooses Primary as the surviving site and the Primary LUN continues to serve I/O to the Host. All the paths from the secondary cluster report Illegal request / LU not found for all I/O commands.
Now say there’s a double failure with the intersite link down and the mediator going down (either simultaneously or sequentially in the below order):
Primary to ONTAP Mediator is down
Primary to Secondary link down (relationship if out of sync) and
Due to the OOS event in this case, the primary cluster needs to re-establish consensus with agreement from either the Mediator or the peer cluster. But since neither is reachable, it cannot establish consensus to serve I/O. Thereby, there will be DISRUPTION
Although another scenario where the intersite link failure first occurs, the relationship would go out of sync. Site A gets consensus via the ONTAP Mediator, and continues to be the Primary CG and serves IO
And now if the ONTAP Mediator fails after the failover/switchover process, the second failure will have no impact except that you cannot perform planned or unplanned events during the time that the ONTAP Mediator is down.

## Slide 24: Disaster at site A
Mediator
C1
Primary
C2
Secondary
NetApp® SnapMirror ® business continuity (SM-BC) detects failure at primary and triggers an automatic failover
When C1 recovers, automatic resync completes to bring the C2 > C1 relationship in sync
Planned failback to restore normal steady-state operations
Parameter | Details
SM-BC action upon failure | Automatic unplanned failover (AUFO)
Host access to storage | C2 after consensus (mirror copy > active copy)
SM-BC relationship state | Out of sync
Failover operation | Possible
Notes: Disaster at Site A
The ONTAP Mediator detects that the primary has gone down due to a disaster, it informs the Secondary site and the Secondary LUN continues to serve I/O to the host. There is a change in the RTPG data reported to the host with the path from the secondary LUN owning node changes to Active-Optimized while all other paths are Non-optimized.
Note: The reverse relationship configuration i.e vs1:/cg/dst as the source and vs0:/cg/src as the destination, will be created as a dormant or hidden entry upfront during the initialize of the forward relationship. The reverse relationship will be activated upon a planned failover or a recovery from unplanned failover. The reverse relationship will not be visible until then. Similarly the forward relationship will be made dormant during this transition.

## Slide 25: Disaster at site B
When C2 recovers, automatic resync completes to bring the C1 > C2 relationship in sync
Mediator
C1
Primary
C2
Secondary
Parameter | Details
NetApp® SnapMirror® business continuity (SM-BC) action upon failure | No action
Host access to storage | C1 after consensus
SM-BC relationship state | Out of sync
Failover operation | n/a
Notes: Same will be the scenario for simultaneous failures of link to Site B and intersite link failure

## Slide 26: ONTAP Mediator failure
Mediator
C1
Primary
C2
Secondary
NetApp® ONTAP® Mediator failure
  Virtual machine (VM)
  Link (single or double)
1
1
2
2
2
Parameter | Details
NetApp SnapMirror® business continuity (SM-BC) action upon failure | n/a
Host access to storage | C1, C2 (no disruption to I/O)
SM-BC relationship state | In sync
Failover operation | Not possible (planned or unplanned failover)
Notes: Manual – tools?

## Slide 27
 | Failure Scenarios | Behavior
1 | Loss of Storage Array (All Nodes) | Seamless failover initiated by Mediator. Database is up. No IO disruption
2 | Loss of one of the storage controller | The partner node in the HA cluster will attempt for takeover. If takeover fails, Mediator performs switchover to remote cluster
3 | Loss of connectivity between Sites | Mediator recognizes this split-brain scenario and resumes the Oracle IO on the node that holds the master copy. When the connectivity between site is back online, the alternate site performs automatic resync
4 | Loss of Disks | Oracle continues to perform IO up to 3 consecutive Disk's failure . This is part of RAID-TEC
5 | Loss of Mediator | Automated unplanned / planned failover and failback is not possible, but the Oracle IO continue to happen and will remain in sync with the remote cluster
6 | Loss of remote DR Storage Cluster | No IO disruption. There will be a momentary pause due to network causing sync replication to abort and Master establishing that it is the rightful owner to continue to serve I/O (consensus) and for that there will be a I/O pause of a couple of seconds and then the I/O will resume. There will be an automatic resync when the site is online

## Slide 28
No | Failure Scenarios | Behavior
1 | Loss of Entire Site ( Host + Storage + Network) | In the absence of Extended RAC, you need to have passive RAC setup/standalone oracle binaries on the remote site that is already zoned or connected . Post storage failover, re-discover the storage devices, mount, recover and bring up the database .
2 | Loss of Entire Site in Extended RAC (RAC node + Storage + Network) | Seamless failover, No IO disruption. If RAC DB service is enabled for Transparent application continuity and failover, the DML replay will happen on the same session from surviving RAC Instance.

## Slide 29
No | Failure Scenarios | Behavior
1 | Loss of Storage Array (All Nodes) | Seamless failover of Database storage to DR site initiated by Mediator. It doesn’t crash the database during the path transition and resumes the IO in few seconds.
2 | Loss of one of the storage controller | The partner node in the HA cluster will attempt for takeover. If takeover fails, Mediator notices both the storage nodes are offline and performs switchover to remote cluster
3 | Loss of connectivity between sites | Mediator recognizes this split-brain scenario and resumes the Oracle IO on the node that holds the master copy. When the connectivity between site is back online, the alternate site performs automatic resync
4 | Loss of Disks | Oracle continues to perform IO up to 3 consecutive Disk's failure . This is part of RAID-TEC
5 | Loss of Fiber Channel Switch | The oracle operations continues to operate from the redundant FC switch at each site. Switch level redundancy is essential, so we have multiple paths to the same storage device at each site.
6 | Loss of Mediator | Automated unplanned and planned failover and failback is not possible, but the Oracle IO continue to happen and will remain in sync with the remote cluster
7 | Loss of remote DR Storage Cluster | There will be no I/O disruption. There will be a momentary pause due to network causing sync replication to abort and Master establishing that it is the rightful owner to continue to serve I/O (consensus) and for that there will be a I/O pause of a couple of seconds and then the I/O will resume. There will be an automatic resync when the site is online
8 | Loss of Entire Site ( Host + Storage + Network) | Without Extended RAC, you need to have passive RAC setup on the remote site that is already zoned or connected . Post storage failover, re-discover the storage devices, mount and recover the database completely.
9 | Loss of Entire Site in Extended RAC (RAC node + Primary storage + Network) | Seamless failover, IO resumes after a few seconds of pause. If RAC DB service is enabled for Transparent application continuity and failover, the DML replay will happen on the same session from surviving RAC Instance

## Slide 30: SnapMirror Business Continuity (SM-BC)
Two-node cluster only, either NetApp® AFF or All SAN Array (ASA)
  No intermixing
10ms round-trip time (RTT) between sites
  Approximately ~150 Km
Up to five consistency groups (CGs) (each with up to 12 volumes)
Total of 60 concurrent synchronous relationships (includes CGs)
NetApp® ONTAP Mediator on Linux server/virtual machine (VM)
Licensing – data protection bundle/premium bundle
Single Lun performance enhancement is not applied for SMBC
NetApp ONTAP FlexGroup volumes, FabricPool storage tiers, NetApp SnapLock,Quality of service (QoS) throughput floor
Maximums, & Supportability & Limitations
Notes: SnapMirror Business Continuity (SM-BC) feature is available via Data ONTAP 9.8. No separate installation is required.
SM-BC topology:
The SM-BC active-active contains two storage systems running version 9.8 or above, with a ONTAP Mediator VM at a 3rd site.
The storage systems are connected via an TCP/IP-based replication link and network to serve all types of replicas.
The ONTAP Mediator is a lightweight software deployed as a on-prem VM in a separate failure domain (3rd site), for purpose of redundancy in case of site failure.
The maximum number of SnapMirror Synchronous Consistency Group relationships in a cluster is limited to 5.
The maximum number of volumes supported per SnapMirror Synchronous Consistency Group relationships is limited to 12.
This limit is platform independent.
SM-BC is built into ONTAP and hence leverages the value of the ONTAP portfolio
You can consolidate all your business critical workloads, nature of IO requirements

## Slide 31: SMBC Comparisons

## Slide 32: Technical considerations (cont.)
Dimension | Functionality in NetApp® SnapMirror Synchronous (SM-S) | Functionality in SnapMirror Business Continuity (SM-BC)
Platforms | All shipping NetApp AFF and FAS platforms with >= 16GB memory ONTAP Select | Any AFF (All SAN Array [ASA] included) platforms
Cluster size | No limit | Two-node primary; two-node secondary No intermixing
Protocols | FC, iSCSI, NFSv3, NFSv4, CIFS/SMB 2.0+, NVMe (all) | FC, iSCSI
Scale | Number of concurrently replicated volumes per HA-pair: AFF=80, FAS=40, Select=20 (includes asynchronous relationships as well as synchronous) | Number of concurrently replicated volumes per HA-pair: AFF=60 (includes asynchronous relationships as well as synchronous)
Network RTT | <10ms RTT (~150Km), LAN, MAN | 
Management | ONTAP System Manager | 
Release interoperability | ONTAP 9.5 and later Future releases will be the same as NetApp SnapMirror® asynchronous, such as previous five releases later or equal to 9.5 | ONTAP 9.8 and later Future releases will be the same as SnapMirror asynchronous, such as the previous five releases later than ONTAP 9.8 (for example, 9.12 works with 9.11, 9.10, 9.9, 9.8, but not with 9.7)
** No commitment, guarantee, or promise on future release content.
Features may be delivered in earlier releases if possible, or in later release where necessary.
Operational

## Slide 33: Technical considerations (cont.)
Dimension | Functionality in NetApp® SnapMirror Synchronous (SM-S) | Functionality in SnapMirror Business Continuity (SM-BC)
Topologies | P2P Fan-out (one sync and one async relationship per volume) Cascade (first sync leg and second async leg per volume) | TAF is point-to-point; no fan-out or cascade Fan-out (one sync and one async relationship per volume)
Nondisruptive operation (NDO) support |  | 
** No commitment, guarantee, or promise for future release content.
Resilience and data protection

## Slide 34: Technical considerations (cont.)
Dimension | Functionality in NetApp® SnapMirror Synchronous (SM-S) | Functionality in SnapMirror Business Continuity (SM-BC)
Topologies | P2P Fan-out (one sync and one async relationship per volume) Cascade (first sync leg and second async leg per volume) | TAF is point-to-point; no fan-out or cascade Fan-out (one sync and one async relationship per volume)
** No commitment, guarantee, or promise for future release content.
Data protection

## Slide 35: Comparing NetApp synchronous replication offerings
SnapMirror Business continuity
Zero Data loss (RPO=0)
  For the application
Automated failover using ONTAP Mediator
Controller, storage, network agnostic
  Customer selects configuration
  IP transport
  Application automated failover is point-to-point
SnapMirror Synchronous Synchronous replication
Zero Data loss (RPO=0)
  For selectable volumes
Manual application failover
Controller, storage, network agnostic
  Customer selects configuration
  IP transport
  Individual volume fan-out and cascade
No CG for Multi-volume environment
Different functionality for different customer needs
TR-4832: Three-way Disaster Recovery Using SnapMirror

## Slide 36
Thanks

## Slide 37: Storage access through multiple failure scenarios
C1 | C2 | Replication link | Mediator | Data access through
Down | Up (mirror) | Up | Down | C2
Down | Up (mirror) | Up | Down | I/O disruption
Up (primary) | Up (mirror) | Down | Down | C1 after consensus
Up (primary) | Up (mirror) | Down | Down | I/O disruption
Up (primary) | Down | Up | Down | C1 after consensus
Up (primary) | Down | Up | Down | I/O disruption
1
2
2
1
1
2
2
1
1
2
2
1
Mediator
C1
C2
Notes: * These rows refer to simultaneous failures of other components while the mediator is unavailable. If the mediator becomes unavailable after an array failure or a replication link failure has already been sustained, then access to storage will remain available on one array as the mediator is not required to resolve the situation. * If the mediator becomes unavailable to both arrays for at least 5 minutes prior to the replication network links failing then the pre-elected array will keep stretched pod volumes online.

## Slide 38: Business continuity solutions
SM-BC versus MetroCluster

## Slide 39: Integrated ONTAP continuous availability
SM-BC
MetroCluster
Continuous Availability for select SAN applications
Minimize cost by tailoring configuration to your requirement
Simplify application management with granular control
Continuous Availability infrastructure
Consolidate critical SAN and NAS workloads on a dedicated solution
Deliver bullet-proof reliability and performance at scale
MetroCluster
SnapMirror Business Continuity (SM-BC)

## Slide 40: Resources
40

## Slide 41: Resources
Documentation for the SnapMirror Business Continuity solution
  https://docs.netapp.com/us-en/ontap/smbc/index.html
ONTAP 9 Documentation
  http://docs.netapp.com/ontap-9/index.jsp
SnapMirror Business Continuity (SM-BC) FAQ
  https://fieldportal.netapp.com/content/1232901?assetComponentId=1235397&languageCode=en-US&nid=9338852
TR-4878: SnapMirror Business Continuity (SM-BC) for ONTAP 9.8
  https://fieldportal.netapp.com/content/1292249?assetComponentId=1294798
Learn more about SnapMirror Business Continuity (SM-BC)

## Slide 42: What is business continuity (BC)?
Notes: Business Continuity, what does this really mean?

## Slide 43: Business continuity and disaster recovery timeline
Time
NetApp® Snapshot™ copies
Loss of service
Recovery point objective (RPO)
Recovery time objective (RTO)
Downtime
Limited
Reaction time
Disruptive event
Snapshot copies
Resume service
Notes: At the onset, it’s important to understand Business Continuity and Disaster Recovery timeline with details around “How long your company can afford to be down in the event of a disaster”.
The first step is to identify the metrics of your company’s
Recovery Point Objective (RPO) which is the measurement of the maximum tolerable amount of data loss.
And Recovery Time Objective (RTO) identified by how quickly you need to recover your IT infrastructure and services following a disaster, in order to maintain business continuity.

## Slide 44: What is business continuity?
Tape/VTL vaulting
Tape/VTL backup
Async replication
Sync replication
D2D/D2C backup
Ability for application to fail over to secondary copy in storage, without application reconnect or user disruption
-36
-24
-12
0
12
24
36
48
60
72
Disaster recovery
Backup and recovery
Recovery point objective (RPO) Time period (amount) of lost data
Recovery time objective (RTO) Time required to resume business
Event
Data loss
Recovery time
Business continuity
Sync replication
Guaranteed zero data loss
1
2
3
Transparent application fail over to prevent application disruption
RPO=0 RTO=0
Notes: In the event of a disaster, every business must have a set of recovery strategies in place to protect and restore mission-critical applications as soon as possible. When evaluating the most suitable disaster recovery technology to protect your business-critical data, it’s important to review some of the nomenclature that is being used under the umbrella of data protection and the key metrics such as RPO and RTO.
Recovery point objective (RPO) refers to how much data loss your business application can tolerate.
And recovery time objective (RTO) refers to how fast you can restart a failed application.
Together, they measure or define acceptable business risk. Typically, backup and recovery deals with hours. Disaster recovery often deals with minutes, and what we call “business continuity” is measured in seconds, often with no data loss at all. Your choice depends entirely on your business priorities.

## Slide 45: SMBC Synchronous replication for zero data loss
Write to a master consistency group (CG) results in write to mirror cluster
Master and mirror designation of CG meant to avoid split brain
Host receives ACK only upon writes to both master and mirror
Periodic CG snapshot scheduled on both clusters
Optimal for host to read/write to master CG
An IO to the mirror CG active non-optimized path will be proxied or redirected to the master CG
Host writes op complete only when NVLOG on both clusters written to
Master CG NVRAM
Mirror CG NVRAM
Host write (1)
RACK (3)
NetApp ONTAP WR (2)
Write (2)
ACK (4)
Write (2)
Master CG NVRAM
Host write (1)
ACK (4)
ACK (6)
Proxy write (2)
Write (3)
Mirror CG NVRAM
RACK (5)
Host write to a CG on cluster hosting master copy
Host write to a CG on cluster hosting mirror copy
Write (3)
ALUA
ALUA
Cluster A
Cluster B
Cluster B
Cluster A
Notes: Mirroring all writes to mirrored vols with snapshots taken hourly
ALUA based transparent failover